## Slide 1: Feather Weather Wing

## Slide 2: Feather Weather Wing: What is it?
It is a 0.9-inch x 2.0-inch circuit board that combines four environmental sensors in the Feather Wing form factor.
  Sensirion SHT45 – Humidity & Temperature
  Sensirion SCD41 – CO2, Temperature, & Humidity
    Benefits from an atmospheric air pressure input.
  Sensirion SGP40 – Indoor Air Quality
    Benefits from a humidity input.
  Bosch BMP390 – Atmospheric Air Pressure
4 Layer PCB
Designed using KiCad 9.0
PCB fabricated by OSHPARK

## Slide 3: Feather Specification
The classic size is 0.9-inch X 2.0-inch with a 0.1-inch hole in each corner.
Created by Adafruit.
Can be wider or longer.
Feather Mainboards have a microcontroller.
Accessory boards are called Feather Wings.
Boards stack using a 1x16 header and a 1x12 header.
Link: Feather Specification

## Slide 4: STEMMA QT
4-Pin 1.0mm pitch JST SH Connector: SM04B-SRSS-TB
  Black for GND
  Red for VCC
  Blue for SDA
  Yellow for SCL
VCC is 3V – 5V
Level shifting is used to accommodate 5V I2C logic.
Created by Adafruit
Very similar to the Sparkfun QWIIC system with the addition of level shifting and an LDO.
  https://www.sparkfun.com/qwiic
Adafruit STEMMA QT

## Slide 5: Schematic

## Slide 6: Bill Of Materials (BOM)
Index | Reference | Description | Manufacturer Part Number | Manufacturer Name | Quantity | DNP
1 | C1,C2,C5 | CAP CER 10UF 10V X7R 0805 | C0805C106K8RACTU | KEMET | 3 | 
2 | C3,C4,C6,C7 | CAP CER 0.1UF 10V X7R 0603 | C0603C104K8RACTU | KEMET | 4 | 
3 | C8,C9 | CAP CER 1UF 16V X7R 0603 | C0603C105K4RACTU | KEMET | 2 | 
4 | D1 | LED GREEN DIFFUSED 0603 SMD | KT EELP41.12-S2U1-25-2X4X-5-R18 | ams-OSRAM USA INC. | 1 | 
5 | J1,J2 | CONN HEADER SMD R/A 4POS 1MM | SM04B-SRSS-TB | JST Sales America Inc. | 2 | 
6 | J3 | Conn_01x16 | - | - | 0 | DNP
7 | J4 | Conn_01x12 | - | - | 0 | DNP
8 | Q1 | MOSFET 2N-CH 50V 0.2A SOT363 | BSS138DWQ-7 | Diodes Incorporated | 1 | 
9 | R1,R2,R3,R4,R5,R9,R10 | RES SMD 10K OHM 1% 1/10W 0603 | CRCW060310K0FKEA | Vishay Dale | 7 | 
10 | R7 | RES SMD 4.7 OHM 1% 1/10W 0603 | CRCW06034R70FNEA | Vishay Dale | 1 | 
11 | R8 | RES SMD 10K OHM 1% 1/10W 0603 | - | - | 0 | DNP
12 | U1 | IC REG LINEAR 3.3V 600MA SOT-25 | AP2112K-3.3TRG1 | Diodes Incorporated | 1 | 
13 | U2 | DIGITAL RH/TEMP W/FILTER | SHT45-AD1F-R2 | Sensirion AG | 1 | 
14 | U3 | SENSOR AIR QUALITY I2C OUTPUT | SCD41-D-R2 | Sensirion AG | 1 | 
15 | U4 | SENSOR 18.13PSIA 10LGA | BMP390 | Bosch Sensortec | 1 | 
16 | U5 | SENSOR AIR QUALITY I2C OUTPUT | SGP40-D-R4 | Sensirion AG | 1 | 

## Slide 7: PCB Copper Layers
Top: Signal /PWR /GND
Inner 1: 3.3V PWR
Inner 2: GND
Bottom: Signal /PWR /GND

## Slide 8: Stackup: Four Layer OSHPARK

## Slide 9: Data Logging and Visualization
Sensor board is connected to the 40-pin expansion header on a Raspberry Pi
Data is read every minute and stored in an InfluxDB time series database.
The data can be queried and displayed using Grafana.
Grafana dashboards are accessible from a web browser on any device on the same network.

## Slide 10: Grafana Dashboard
Data visualization

## Slide 11: Grafana Dashboard
HUGE Hailstorm on April 27, 2023

## Slide 12: THE END Ben Crockett